TABLE 1. Summary of the density investigations of [OMIM][BF4].

| First author | Ref | Year | Method | Properties | Temperature, T/Kta | Pressure, p/MPa | Uncertainty, (( | F.E. | Purity | IL Source |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Gu | [7] | 2002 | UPDA | ρ, T | 298 and 323 | 0.099 to 206.94 | ± 8 kg∙m-3 (ρ) | Tait | 99% | LP |
| Harris | [8] | 2006 | VTD | ρ, T, η | 273.15 to 353.15 | 0.101 to 224.2 | ±0.05 kg∙m-3 (ρ) | Tait | H2O cont=54 ± 10∙10-6 | LP |
| Gardas | [9] | 2007 | VTD | p, ρ, T, η | 293.15 to 392.15 | 0.101 to 10.0 | ±0.3 kg∙m-3 (ρ) ±0.025 MPa (p), ±0.01 K (T) |  | >99 % H2O cont= 371 ppm | IoLiTec |
| Sanmamed | [10] | 2010 | VTD | p, ρ, T, η | 283.15 to 323.15 | 0.101 to 60 | ±0.30 kg∙m-3 (ρ) ±0.01 K (T), ±0.01 MPa (p) |  | >0.99 mass fr. | SI |
| Tomida | [11] | 2012 | VTD | p, ρ, T, η | 293.15 to 353.15 | 0.101 to 20.0 | 0.2 % (ρ) 10 mK (T), 0.1 MPa (p) | Tait | >98.5 % w.c.<90 ppm | LP |
| Hosseini | [12] | 2013 | Simulated | p, ρ, T, κS | 313 to 452 | 0.101 to 10 | 0.24 % (ρ) |  |  |  |
| Roshan | [13] | 2013 | Simulated | ρ, T | 293.15 to 393.15 | 1 to 10 | 0.10426, 0.199222 (ρ) |  |  |  |
| Ribeiro | [14] | 2014 | GCM | ρ, T, Vm, Tg, pg | 194 and 295 | 2100 and 0.1 |  |  |  | IoLiTec |
| Safarov | [t.w.] | 2016 | VTD | p, ρ, T, η, cp, u | 278.15 to 413.15 | 0.101 to 140 | ±(0.1 to 0.8) kg∙m-3 (ρ) | BRES | w.c.<40 ppm | SA |

taT, temperature; p, pressure; ρ, density; UPDA, ultrahigh-pressure density apparatus; LP – Laboratory product (synthesis); VTD, Vibration tube densimeter; η, Viscosity; SI., Solvent Innovation; cp, heat capacity; u, speed of sound; w.c., water content; κS, isentropic exponent; GCM, group contribution model; BRES, Baku-Rostock equation of state; SA, Sigma-Aldrich; t.w., this work.

TABLE 2.	Experimental values of pressure p/MPa, density ρ/kg(m-3, temperature T/K, together with the calculated values of isothermal compressibility κT(106/MPa-1, isobaric thermal expansibility (p(106/K-1, difference in isobaric and isochoric heat capacities (cp-cv)/J(kg-1(K-1, thermal pressure coefficient γ/MPa(K-1, internal pressure pint/MPa, isobaric heat capacity cp/J(kg-1(K-1, isochoric heat capacity cv/J(kg-1(K-1, speed of sound u/m(s-1 and isentropic exponent κs of [OMIM][BF4].

| p | ρ | T | κT | (p | cp-cv | γ | pint | cp | cv | u | κs |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0.101a | 1117.16 | 278.15 | 413.30 | 611.40 | 225.23 | 1.4794 | 411.40 | 1726.90 | 1501.67 | 1578.39 | 27551.56 |
| 1.002 | 1117.56 | 278.16 | 411.80 | 609.70 | 224.76 | 1.4808 | 410.90 | 1726.74 | 1501.99 | 1580.74 | 2786.420 |
| 5.032 | 1119.33 | 278.15 | 405.10 | 602.40 | 222.64 | 1.4871 | 408.60 | 1725.94 | 1503.29 | 1591.30 | 563.221 |
| 10.002 | 1121.48 | 278.13 | 397.20 | 593.70 | 220.10 | 1.4948 | 405.70 | 1724.92 | 1504.82 | 1604.19 | 288.541 |
| 19.968 | 1125.74 | 278.15 | 382.40 | 577.10 | 215.23 | 1.5094 | 399.90 | 1722.99 | 1507.76 | 1629.30 | 149.669 |
| 29.958 | 1129.91 | 278.14 | 368.60 | 561.60 | 210.57 | 1.5234 | 393.80 | 1720.94 | 1510.37 | 1653.88 | 103.179 |
| 40.002 | 1134.00 | 278.15 | 355.90 | 546.90 | 206.12 | 1.5368 | 387.50 | 1718.86 | 1512.74 | 1677.89 | 79.822 |
| 49.985 | 1137.97 | 278.15 | 344.10 | 533.10 | 201.89 | 1.5495 | 381.00 | 1716.70 | 1514.81 | 1701.20 | 65.896 |
| 60.001 | 1141.86 | 278.17 | 333.10 | 520.10 | 197.83 | 1.5615 | 374.40 | 1714.49 | 1516.66 | 1723.97 | 56.567 |
| 69.987 | 1145.64 | 278.15 | 322.80 | 507.80 | 193.92 | 1.5731 | 367.60 | 1712.09 | 1518.17 | 1746.26 | 49.922 |
| 80.002 | 1149.33 | 278.15 | 313.10 | 496.00 | 190.15 | 1.5841 | 360.60 | 1709.62 | 1519.47 | 1768.08 | 44.913 |
| 89.935 | 1152.89 | 278.16 | 304.20 | 485.00 | 186.55 | 1.5944 | 353.60 | 1707.08 | 1520.53 | 1789.24 | 41.040 |
| 99.924 | 1156.38 | 278.15 | 295.70 | 474.40 | 183.05 | 1.6043 | 346.30 | 1704.37 | 1521.32 | 1810.08 | 37.916 |
| 109.953 | 1159.79 | 278.15 | 287.70 | 464.20 | 179.65 | 1.6136 | 338.90 | 1701.54 | 1521.89 | 1830.61 | 35.347 |
| 119.957 | 1163.09 | 278.13 | 280.10 | 454.50 | 176.34 | 1.6226 | 331.30 | 1698.53 | 1522.20 | 1850.73 | 33.210 |
| 130.005 | 1166.30 | 278.15 | 272.90 | 445.20 | 173.15 | 1.6310 | 323.60 | 1695.50 | 1522.35 | 1870.48 | 31.387 |
| 139.953 | 1169.39 | 278.15 | 266.20 | 436.30 | 170.06 | 1.6388 | 315.90 | 1692.30 | 1522.24 | 1889.72 | 29.839 |
| 0.101 | 1113.71 | 283.15 | 422.50 | 613.10 | 226.28 | 1.4513 | 410.80 | 1736.90 | 1510.62 | 1563.35 | 26946.35 |
| 1.099 | 1114.16 | 283.12 | 420.70 | 611.30 | 225.76 | 1.4532 | 410.30 | 1736.67 | 1510.90 | 1566.11 | 2486.241 |
| 5.074 | 1115.95 | 283.18 | 414.00 | 604.20 | 223.79 | 1.4595 | 408.20 | 1736.11 | 1512.31 | 1576.47 | 546.542 |
| 9.959 | 1118.13 | 283.17 | 405.90 | 595.70 | 221.42 | 1.4676 | 405.60 | 1735.25 | 1513.83 | 1589.28 | 283.571 |
| 19.809 | 1122.45 | 283.16 | 390.60 | 579.50 | 216.84 | 1.4834 | 400.20 | 1733.54 | 1516.70 | 1614.54 | 147.713 |
| 29.992 | 1126.81 | 283.15 | 376.10 | 563.80 | 212.36 | 1.4991 | 394.50 | 1731.74 | 1519.38 | 1639.95 | 101.049 |
| 39.224 | 1130.67 | 283.14 | 363.90 | 550.40 | 208.50 | 1.5128 | 389.10 | 1730.07 | 1521.56 | 1662.39 | 79.667 |
| 50.024 | 1135.07 | 283.14 | 350.60 | 535.80 | 204.22 | 1.5281 | 382.60 | 1728.06 | 1523.85 | 1687.97 | 64.653 |
| 59.544 | 1138.85 | 283.13 | 339.80 | 523.60 | 200.61 | 1.5410 | 376.80 | 1726.21 | 1525.60 | 1709.99 | 55.926 |
| 70.018 | 1142.89 | 283.14 | 328.70 | 511.00 | 196.82 | 1.5547 | 370.20 | 1724.12 | 1527.30 | 1733.60 | 49.054 |
| 79.392 | 1146.41 | 283.15 | 319.40 | 500.30 | 193.57 | 1.5665 | 364.10 | 1722.16 | 1528.60 | 1754.28 | 44.435 |
| 89.988 | 1150.28 | 283.15 | 309.50 | 488.80 | 190.03 | 1.5793 | 357.20 | 1719.82 | 1529.79 | 1777.18 | 40.367 |
| 99.230 | 1153.56 | 283.16 | 301.40 | 479.20 | 187.06 | 1.5900 | 351.00 | 1717.70 | 1530.64 | 1796.73 | 37.523 |
| 109.987 | 1157.26 | 283.16 | 292.50 | 468.60 | 183.72 | 1.6020 | 343.60 | 1715.08 | 1531.36 | 1819.07 | 34.811 |
| 119.006 | 1160.27 | 283.16 | 285.50 | 460.20 | 181.02 | 1.6117 | 337.40 | 1712.78 | 1531.76 | 1837.38 | 32.909 |
| 130.021 | 1163.84 | 283.16 | 277.40 | 450.30 | 177.82 | 1.6231 | 329.60 | 1709.84 | 1532.01 | 1859.38 | 30.943 |
| 139.540 | 1166.81 | 283.16 | 270.80 | 442.10 | 175.14 | 1.6325 | 322.70 | 1707.17 | 1532.02 | 1878.04 | 29.491 |
| 0.101 | 1106.78 | 293.15 | 440.80 | 615.30 | 227.55 | 1.3961 | 409.20 | 1757.32 | 1529.77 | 1534.57 | 25804.64 |
| 1.471 | 1107.42 | 293.16 | 438.20 | 612.90 | 226.92 | 1.3986 | 408.50 | 1757.14 | 1530.23 | 1538.26 | 1781.322 |
| 4.894 | 1109.03 | 293.13 | 431.80 | 606.80 | 225.34 | 1.4051 | 407.00 | 1756.60 | 1531.26 | 1547.67 | 542.810 |
| 9.565 | 1111.20 | 293.14 | 423.50 | 598.70 | 223.25 | 1.4136 | 404.80 | 1755.97 | 1532.72 | 1560.23 | 282.820 |
| 19.598 | 1115.77 | 293.15 | 406.70 | 582.30 | 219.00 | 1.4317 | 400.10 | 1754.63 | 1535.63 | 1586.66 | 143.343 |
| 30.023 | 1120.40 | 293.15 | 390.70 | 566.50 | 214.89 | 1.4499 | 395.00 | 1753.24 | 1538.35 | 1613.36 | 97.149 |
| 39.825 | 1124.63 | 293.16 | 376.90 | 552.70 | 211.26 | 1.4664 | 390.10 | 1751.94 | 1540.68 | 1637.77 | 75.755 |
| 49.979 | 1128.90 | 293.16 | 363.60 | 539.30 | 207.72 | 1.4832 | 384.80 | 1750.55 | 1542.82 | 1662.45 | 62.431 |
| 59.384 | 1132.74 | 293.16 | 352.20 | 527.70 | 204.63 | 1.4983 | 379.90 | 1749.22 | 1544.59 | 1684.77 | 54.146 |
| 70.002 | 1136.95 | 293.16 | 340.20 | 515.40 | 201.32 | 1.5150 | 374.10 | 1747.66 | 1546.34 | 1709.39 | 47.459 |
| 79.597 | 1140.64 | 293.15 | 330.10 | 504.90 | 198.48 | 1.5297 | 368.80 | 1746.16 | 1547.68 | 1731.15 | 42.946 |
| 89.979 | 1144.52 | 293.15 | 319.80 | 494.10 | 195.56 | 1.5451 | 363.00 | 1744.48 | 1548.93 | 1754.18 | 39.140 |
| 99.934 | 1148.11 | 293.16 | 310.60 | 484.40 | 192.89 | 1.5595 | 357.30 | 1742.82 | 1549.93 | 1775.78 | 36.227 |
| 109.976 | 1151.61 | 293.15 | 301.80 | 475.00 | 190.31 | 1.5738 | 351.40 | 1741.00 | 1550.69 | 1797.17 | 33.822 |
| 119.373 | 1154.79 | 293.15 | 294.10 | 466.70 | 188.00 | 1.5868 | 345.80 | 1739.23 | 1551.23 | 1816.81 | 31.933 |
| 129.971 | 1158.24 | 293.15 | 285.90 | 457.80 | 185.50 | 1.6012 | 339.40 | 1737.13 | 1551.64 | 1838.55 | 30.128 |
| 139.266 | 1161.16 | 293.15 | 279.10 | 450.30 | 183.38 | 1.6135 | 333.70 | 1735.19 | 1551.81 | 1857.28 | 28.768 |
| 0.101 | 1103.47 | 298.15 | 450.00 | 616.10 | 227.95 | 1.3692 | 408.10 | 1767.74 | 1539.79 | 1520.70 | 25262.03 |
| 1.023 | 1103.90 | 298.15 | 448.10 | 614.40 | 227.53 | 1.3710 | 407.70 | 1767.61 | 1540.09 | 1523.27 | 2503.586 |
| 5.041 | 1105.81 | 298.14 | 440.40 | 607.20 | 225.73 | 1.3788 | 406.00 | 1767.05 | 1541.32 | 1534.43 | 516.463 |
| 10.002 | 1108.13 | 298.15 | 431.20 | 598.60 | 223.60 | 1.3883 | 403.90 | 1766.43 | 1542.83 | 1547.90 | 265.459 |
| 19.985 | 1112.73 | 298.13 | 413.90 | 582.40 | 219.55 | 1.4071 | 399.50 | 1765.14 | 1545.59 | 1574.61 | 138.063 |
| 29.935 | 1117.19 | 298.15 | 398.10 | 567.40 | 215.80 | 1.4252 | 395.00 | 1763.97 | 1548.17 | 1600.39 | 95.600 |
| 40.004 | 1121.59 | 298.16 | 383.40 | 553.40 | 212.27 | 1.4432 | 390.30 | 1762.78 | 1550.51 | 1625.81 | 74.118 |
| 49.923 | 1125.81 | 298.15 | 370.00 | 540.40 | 209.02 | 1.4605 | 385.50 | 1761.57 | 1552.55 | 1650.26 | 61.421 |
| 60.008 | 1129.98 | 298.16 | 357.40 | 528.10 | 205.92 | 1.4777 | 380.60 | 1760.35 | 1554.43 | 1674.48 | 52.802 |
| 70.003 | 1134.00 | 298.15 | 345.80 | 516.70 | 203.02 | 1.4944 | 375.60 | 1759.05 | 1556.03 | 1697.96 | 46.706 |
| 79.985 | 1137.90 | 298.13 | 334.90 | 506.00 | 200.29 | 1.5108 | 370.40 | 1757.69 | 1557.40 | 1720.91 | 42.133 |
| 89.924 | 1141.66 | 298.15 | 324.80 | 495.90 | 197.73 | 1.5267 | 365.30 | 1756.36 | 1558.64 | 1743.19 | 38.578 |
| 99.985 | 1145.36 | 298.16 | 315.30 | 486.30 | 195.27 | 1.5425 | 359.90 | 1754.93 | 1559.66 | 1765.30 | 35.697 |
| 110.006 | 1148.92 | 298.15 | 306.30 | 477.20 | 192.93 | 1.5580 | 354.50 | 1753.38 | 1560.45 | 1786.92 | 33.349 |
| 120.004 | 1152.37 | 298.14 | 297.90 | 468.60 | 190.71 | 1.5731 | 349.00 | 1751.74 | 1561.04 | 1808.09 | 31.393 |
| 129.957 | 1155.68 | 298.15 | 290.00 | 460.40 | 188.61 | 1.5879 | 343.50 | 1750.08 | 1561.48 | 1828.73 | 29.742 |
| 139.954 | 1158.89 | 298.15 | 282.50 | 452.70 | 186.59 | 1.6025 | 337.80 | 1748.30 | 1561.71 | 1849.13 | 28.317 |
| 0.101 | 1093.31 | 313.15 | 477.80 | 617.90 | 228.89 | 1.2932 | 404.90 | 1799.86 | 1570.96 | 1481.04 | 23740.74 |
| 1.930 | 1094.23 | 313.13 | 473.70 | 614.50 | 228.11 | 1.2971 | 404.20 | 1799.54 | 1571.44 | 1486.41 | 1252.525 |
| 5.032 | 1095.77 | 313.16 | 467.10 | 608.80 | 226.82 | 1.3035 | 403.20 | 1799.17 | 1572.35 | 1495.29 | 486.857 |
| 9.821 | 1098.14 | 313.18 | 457.10 | 600.40 | 224.90 | 1.3134 | 401.50 | 1798.56 | 1573.67 | 1508.89 | 254.571 |
| 19.940 | 1103.04 | 313.18 | 437.50 | 583.80 | 221.12 | 1.3342 | 397.90 | 1797.30 | 1576.17 | 1537.09 | 130.704 |
| 30.024 | 1107.79 | 313.17 | 419.70 | 568.50 | 217.71 | 1.3547 | 394.20 | 1796.13 | 1578.42 | 1564.41 | 90.308 |
| 39.958 | 1112.35 | 313.16 | 403.60 | 554.70 | 214.64 | 1.3744 | 390.50 | 1795.06 | 1580.42 | 1590.52 | 70.428 |
| 49.979 | 1116.81 | 313.16 | 388.70 | 541.80 | 211.80 | 1.3941 | 386.60 | 1794.06 | 1582.26 | 1616.20 | 58.371 |
| 59.850 | 1121.08 | 313.15 | 375.10 | 530.00 | 209.23 | 1.4132 | 382.70 | 1793.08 | 1583.85 | 1640.89 | 50.434 |
| 70.004 | 1125.34 | 313.15 | 362.10 | 518.70 | 206.80 | 1.4326 | 378.60 | 1792.12 | 1585.32 | 1665.66 | 44.597 |
| 79.915 | 1129.36 | 313.15 | 350.30 | 508.40 | 204.61 | 1.4512 | 374.50 | 1791.18 | 1586.57 | 1689.29 | 40.325 |
| 90.030 | 1133.34 | 313.15 | 339.10 | 498.60 | 202.54 | 1.4701 | 370.30 | 1790.21 | 1587.67 | 1712.89 | 36.930 |
| 98.725 | 1136.66 | 313.16 | 330.10 | 490.60 | 200.89 | 1.4861 | 366.70 | 1789.38 | 1588.49 | 1732.76 | 34.563 |
| 109.978 | 1140.80 | 313.16 | 319.20 | 480.90 | 198.90 | 1.5066 | 361.80 | 1788.25 | 1589.35 | 1757.98 | 32.053 |
| 120.378 | 1144.48 | 313.17 | 309.70 | 472.40 | 197.21 | 1.5253 | 357.30 | 1787.19 | 1589.98 | 1780.79 | 30.147 |
| 129.996 | 1147.76 | 313.16 | 301.50 | 465.10 | 195.74 | 1.5426 | 353.10 | 1786.12 | 1590.38 | 1801.53 | 28.655 |
| 139.395 | 1150.85 | 313.16 | 293.90 | 458.20 | 194.40 | 1.5592 | 348.90 | 1785.06 | 1590.65 | 1821.43 | 27.393 |
| 0.101 | 1079.64 | 333.15 | 516.50 | 622.30 | 231.32 | 1.2047 | 401.30 | 1844.64 | 1613.32 | 1431.86 | 21916.88 |
| 1.733 | 1080.53 | 333.15 | 512.30 | 619.00 | 230.62 | 1.2084 | 400.80 | 1844.28 | 1613.66 | 1436.89 | 1287.402 |
| 5.048 | 1082.30 | 333.15 | 503.90 | 612.60 | 229.26 | 1.2159 | 400.00 | 1843.59 | 1614.33 | 1447.03 | 448.985 |
| 9.927 | 1084.89 | 333.16 | 492.10 | 603.60 | 227.35 | 1.2267 | 398.80 | 1842.65 | 1615.30 | 1461.72 | 233.540 |
| 19.736 | 1089.98 | 333.15 | 470.00 | 586.70 | 223.84 | 1.2484 | 396.20 | 1840.86 | 1617.02 | 1490.63 | 122.739 |
| 29.988 | 1095.14 | 333.15 | 449.10 | 570.70 | 220.57 | 1.2708 | 393.40 | 1839.21 | 1618.64 | 1519.91 | 84.378 |
| 39.557 | 1099.81 | 333.15 | 431.30 | 557.00 | 217.86 | 1.2915 | 390.70 | 1837.83 | 1619.97 | 1546.45 | 66.500 |
| 50.011 | 1104.76 | 333.16 | 413.50 | 543.20 | 215.21 | 1.3137 | 387.70 | 1836.48 | 1621.27 | 1574.65 | 54.776 |
| 59.751 | 1109.22 | 333.17 | 398.30 | 531.40 | 213.00 | 1.3343 | 384.80 | 1835.33 | 1622.33 | 1600.24 | 47.537 |
| 69.979 | 1113.74 | 333.16 | 383.60 | 520.00 | 210.92 | 1.3558 | 381.70 | 1834.17 | 1623.24 | 1626.44 | 42.097 |
| 79.790 | 1117.93 | 333.16 | 370.50 | 509.90 | 209.13 | 1.3762 | 378.70 | 1833.14 | 1624.00 | 1651.00 | 38.185 |
| 90.004 | 1122.14 | 333.15 | 357.80 | 500.00 | 207.46 | 1.3973 | 375.50 | 1832.10 | 1624.63 | 1676.02 | 35.015 |
| 99.766 | 1126.01 | 333.14 | 346.60 | 491.20 | 206.03 | 1.4174 | 372.40 | 1831.15 | 1625.12 | 1699.41 | 32.589 |
| 109.994 | 1129.91 | 333.14 | 335.60 | 482.60 | 204.69 | 1.4383 | 369.20 | 1830.21 | 1625.52 | 1723.41 | 30.506 |
| 118.728 | 1133.11 | 333.14 | 326.70 | 475.70 | 203.66 | 1.4560 | 366.30 | 1829.42 | 1625.76 | 1743.51 | 29.009 |
| 129.979 | 1137.06 | 333.14 | 316.00 | 467.40 | 202.48 | 1.4788 | 362.70 | 1828.43 | 1625.96 | 1768.92 | 27.374 |
| 139.759 | 1140.34 | 333.15 | 307.40 | 460.50 | 201.57 | 1.4984 | 359.40 | 1827.60 | 1626.04 | 1790.57 | 26.165 |
| 0.101 | 1066.28 | 353.15 | 558.00 | 631.10 | 236.43 | 1.1311 | 399.30 | 1891.56 | 1655.14 | 1385.95 | 20278.39 |
| 1.702 | 1067.20 | 353.15 | 553.10 | 627.70 | 235.74 | 1.1349 | 399.10 | 1891.06 | 1655.32 | 1391.18 | 1213.546 |
| 4.947 | 1069.04 | 353.15 | 543.50 | 621.00 | 234.38 | 1.1426 | 398.60 | 1890.07 | 1655.69 | 1401.70 | 424.606 |
| 10.078 | 1071.92 | 353.16 | 529.00 | 610.80 | 232.36 | 1.1548 | 397.70 | 1888.59 | 1656.23 | 1418.05 | 213.905 |
| 19.928 | 1077.32 | 353.16 | 503.30 | 592.80 | 228.85 | 1.1778 | 396.00 | 1885.93 | 1657.08 | 1448.68 | 113.474 |
| 30.004 | 1082.68 | 353.16 | 479.70 | 576.20 | 225.70 | 1.2012 | 394.20 | 1883.46 | 1657.76 | 1478.99 | 78.944 |
| 40.055 | 1087.84 | 353.16 | 458.30 | 561.10 | 222.95 | 1.2241 | 392.30 | 1881.22 | 1658.27 | 1508.30 | 61.792 |
| 49.978 | 1092.78 | 353.15 | 439.20 | 547.50 | 220.55 | 1.2466 | 390.30 | 1879.15 | 1658.60 | 1536.42 | 51.617 |
| 59.854 | 1097.53 | 353.16 | 421.80 | 535.10 | 218.45 | 1.2687 | 388.20 | 1877.29 | 1658.84 | 1563.61 | 44.829 |
| 69.987 | 1102.23 | 353.15 | 405.30 | 523.40 | 216.54 | 1.2912 | 386.00 | 1875.47 | 1658.92 | 1590.83 | 39.852 |
| 80.761 | 1107.03 | 353.14 | 389.30 | 511.90 | 214.77 | 1.3150 | 383.60 | 1873.66 | 1658.90 | 1619.04 | 35.924 |
| 90.004 | 1110.99 | 353.15 | 376.60 | 502.80 | 213.43 | 1.3351 | 381.50 | 1872.25 | 1658.81 | 1642.64 | 33.299 |
| 99.542 | 1114.93 | 353.15 | 364.40 | 494.00 | 212.21 | 1.3559 | 379.30 | 1870.84 | 1658.63 | 1666.51 | 31.100 |
| 110.030 | 1119.09 | 353.16 | 351.90 | 485.00 | 211.04 | 1.3785 | 376.80 | 1869.40 | 1658.36 | 1692.11 | 29.115 |
| 119.712 | 1122.75 | 353.17 | 341.10 | 477.30 | 210.11 | 1.3992 | 374.50 | 1868.14 | 1658.04 | 1715.30 | 27.591 |
| 130.002 | 1126.48 | 353.16 | 330.40 | 469.60 | 209.23 | 1.4212 | 371.90 | 1866.83 | 1657.59 | 1739.49 | 26.219 |
| 139.720 | 1129.83 | 353.16 | 320.90 | 462.80 | 208.53 | 1.4419 | 369.50 | 1865.66 | 1657.13 | 1761.89 | 25.108 |
| 0.101 | 1053.09 | 373.15 | 602.50 | 644.00 | 243.98 | 1.0689 | 398.70 | 1940.61 | 1696.62 | 1342.86 | 18796.03 |
| 1.917 | 1054.17 | 373.14 | 596.00 | 639.90 | 243.22 | 1.0736 | 398.70 | 1939.87 | 1696.64 | 1349.17 | 1000.723 |
| 5.136 | 1056.07 | 373.15 | 584.90 | 632.80 | 241.93 | 1.0819 | 398.60 | 1938.66 | 1696.72 | 1360.19 | 380.364 |
| 10.024 | 1058.92 | 373.14 | 568.80 | 622.50 | 240.08 | 1.0945 | 398.40 | 1936.81 | 1696.73 | 1376.71 | 200.216 |
| 19.898 | 1064.55 | 373.15 | 539.10 | 603.40 | 236.73 | 1.1193 | 397.80 | 1933.36 | 1696.63 | 1409.03 | 106.231 |
| 30.014 | 1070.14 | 373.16 | 511.90 | 585.80 | 233.75 | 1.1444 | 397.00 | 1930.05 | 1696.31 | 1441.03 | 74.054 |
| 39.630 | 1075.28 | 373.17 | 488.70 | 570.70 | 231.27 | 1.1679 | 396.20 | 1927.09 | 1695.83 | 1470.46 | 58.680 |
| 49.974 | 1080.64 | 373.16 | 466.00 | 555.90 | 228.92 | 1.1928 | 395.10 | 1924.04 | 1695.12 | 1501.18 | 48.739 |
| 60.128 | 1085.71 | 373.16 | 445.90 | 542.60 | 226.91 | 1.2169 | 394.00 | 1921.22 | 1694.30 | 1530.43 | 42.298 |
| 70.024 | 1090.48 | 373.16 | 427.90 | 530.70 | 225.20 | 1.2402 | 392.80 | 1918.60 | 1693.40 | 1558.14 | 37.810 |
| 80.421 | 1095.30 | 373.17 | 410.70 | 519.20 | 223.63 | 1.2642 | 391.40 | 1916.00 | 1692.38 | 1586.48 | 34.279 |
| 90.019 | 1099.58 | 373.18 | 396.00 | 509.40 | 222.35 | 1.2862 | 390.00 | 1913.71 | 1691.36 | 1611.99 | 31.740 |
| 98.752 | 1103.34 | 373.19 | 383.60 | 501.00 | 221.33 | 1.3061 | 388.70 | 1911.71 | 1690.38 | 1634.69 | 29.855 |
| 109.976 | 1107.97 | 373.17 | 368.80 | 491.00 | 220.16 | 1.3314 | 386.90 | 1909.18 | 1689.02 | 1663.27 | 27.871 |
| 119.510 | 1111.73 | 373.15 | 357.10 | 483.00 | 219.30 | 1.3527 | 385.30 | 1907.12 | 1687.82 | 1687.00 | 26.477 |
| 130.034 | 1115.70 | 373.16 | 345.10 | 474.90 | 218.49 | 1.3760 | 383.40 | 1904.99 | 1686.50 | 1712.62 | 25.171 |
| 138.874 | 1118.88 | 373.16 | 335.70 | 468.40 | 217.90 | 1.3954 | 381.80 | 1903.27 | 1685.37 | 1733.66 | 24.224 |
| 0.101 | 1039.55 | 393.15 | 649.20 | 657.40 | 251.89 | 1.0127 | 398.00 | 1991.79 | 1739.90 | 1302.65 | 17458.29 |
| 1.276 | 1040.29 | 393.15 | 644.30 | 654.70 | 251.49 | 1.0161 | 398.20 | 1991.33 | 1739.84 | 1306.95 | 1392.096 |
| 5.086 | 1042.67 | 393.17 | 629.10 | 646.10 | 250.27 | 1.0270 | 398.70 | 1989.93 | 1739.66 | 1320.73 | 357.517 |
| 10.377 | 1045.93 | 393.18 | 609.10 | 634.70 | 248.68 | 1.0421 | 399.40 | 1987.95 | 1739.28 | 1339.52 | 180.840 |
| 20.336 | 1051.92 | 393.15 | 574.80 | 615.10 | 245.99 | 1.0701 | 400.40 | 1984.17 | 1738.18 | 1373.90 | 97.652 |
| 29.978 | 1057.53 | 393.13 | 545.40 | 598.10 | 243.74 | 1.0966 | 401.10 | 1980.61 | 1736.87 | 1405.95 | 69.747 |
| 40.097 | 1063.23 | 393.12 | 517.80 | 581.90 | 241.69 | 1.1237 | 401.60 | 1976.98 | 1735.29 | 1438.34 | 54.870 |
| 50.015 | 1068.63 | 393.13 | 493.60 | 567.40 | 239.95 | 1.1497 | 402.00 | 1973.53 | 1733.58 | 1469.03 | 46.117 |
| 60.161 | 1073.96 | 393.14 | 471.10 | 553.90 | 238.39 | 1.1758 | 402.10 | 1970.07 | 1731.68 | 1499.46 | 40.140 |
| 69.971 | 1078.92 | 393.14 | 451.40 | 541.90 | 237.06 | 1.2005 | 402.00 | 1966.76 | 1729.70 | 1528.03 | 36.002 |
| 80.150 | 1083.87 | 393.13 | 432.60 | 530.40 | 235.83 | 1.2258 | 401.80 | 1963.37 | 1727.53 | 1556.86 | 32.774 |
| 90.030 | 1088.49 | 393.14 | 416.00 | 520.00 | 234.79 | 1.2500 | 401.40 | 1960.19 | 1725.39 | 1584.08 | 30.334 |
| 99.120 | 1092.57 | 393.15 | 401.80 | 511.10 | 233.94 | 1.2718 | 400.90 | 1957.32 | 1723.37 | 1608.52 | 28.514 |
| 109.998 | 1097.25 | 393.13 | 386.20 | 501.10 | 233.02 | 1.2977 | 400.20 | 1953.88 | 1720.86 | 1637.10 | 26.730 |
| 119.495 | 1101.15 | 393.12 | 373.50 | 493.00 | 232.31 | 1.3199 | 399.40 | 1950.97 | 1718.66 | 1661.46 | 25.435 |
| 130.004 | 1105.26 | 393.13 | 360.50 | 484.50 | 231.63 | 1.3441 | 398.40 | 1947.87 | 1716.24 | 1687.80 | 24.219 |
| 138.906 | 1108.58 | 393.14 | 350.20 | 477.70 | 231.11 | 1.3644 | 397.50 | 1945.31 | 1714.20 | 1709.64 | 23.331 |
| 0.101 | 1025.75 | 413.15 | 695.50 | 664.90 | 256.15 | 0.9561 | 394.90 | 2045.08 | 1788.93 | 1266.09 | 16275.33 |
| 2.678 | 1027.45 | 413.13 | 683.30 | 659.30 | 255.81 | 0.9648 | 395.90 | 2044.46 | 1788.65 | 1276.03 | 624.612 |
| 4.989 | 1028.97 | 413.15 | 672.90 | 654.40 | 255.52 | 0.9724 | 396.80 | 2043.99 | 1788.48 | 1284.78 | 340.421 |
| 9.857 | 1032.13 | 413.19 | 652.10 | 644.40 | 254.95 | 0.9883 | 398.50 | 2042.94 | 1787.99 | 1302.91 | 177.764 |
| 19.284 | 1038.12 | 413.14 | 615.20 | 626.70 | 253.99 | 1.0187 | 401.60 | 2040.34 | 1786.36 | 1337.12 | 96.275 |
| 30.020 | 1044.71 | 413.16 | 578.40 | 608.50 | 253.10 | 1.0520 | 404.60 | 2037.32 | 1784.22 | 1374.39 | 65.758 |
| 40.114 | 1050.68 | 413.18 | 547.90 | 593.10 | 252.41 | 1.0825 | 407.20 | 2034.26 | 1781.85 | 1408.05 | 51.945 |
| 50.025 | 1056.34 | 413.16 | 521.00 | 579.30 | 251.82 | 1.1118 | 409.30 | 2030.95 | 1779.13 | 1439.99 | 43.797 |
| 60.345 | 1062.02 | 413.14 | 495.90 | 566.00 | 251.29 | 1.1414 | 411.20 | 2027.36 | 1776.07 | 1472.15 | 38.147 |
| 69.986 | 1067.12 | 413.14 | 474.70 | 554.60 | 250.87 | 1.1684 | 412.70 | 2023.97 | 1773.10 | 1501.16 | 34.361 |
| 80.230 | 1072.32 | 413.13 | 454.10 | 543.30 | 250.47 | 1.1964 | 414.10 | 2020.23 | 1769.77 | 1531.13 | 31.331 |
| 89.976 | 1077.08 | 413.13 | 436.20 | 533.30 | 250.12 | 1.2225 | 415.10 | 2016.65 | 1766.52 | 1558.83 | 29.084 |
| 99.285 | 1081.43 | 413.12 | 420.50 | 524.30 | 249.81 | 1.2469 | 415.80 | 2013.15 | 1763.34 | 1584.63 | 27.345 |
| 110.011 | 1086.22 | 413.12 | 403.80 | 514.60 | 249.49 | 1.2744 | 416.50 | 2009.12 | 1759.64 | 1613.56 | 25.702 |
| 120.014 | 1090.47 | 413.11 | 389.50 | 506.10 | 249.19 | 1.2995 | 416.80 | 2005.32 | 1756.13 | 1639.87 | 24.431 |
| 129.986 | 1094.50 | 413.13 | 376.20 | 498.10 | 248.93 | 1.3240 | 417.00 | 2001.62 | 1752.70 | 1665.45 | 23.355 |
| 139.746 | 1098.25 | 413.15 | 364.10 | 490.60 | 248.68 | 1.3475 | 417.00 | 1998.02 | 1749.34 | 1689.92 | 22.447 |

a 	Standard uncertainties u are u(T) = 0.015 K, u(p) = 0.1 MPa for p < 100 MPa, u(p) = 0.25 MPa for p > 100 MPa, and the combined expanded uncertainty Uc is Uc(ρ) = 0.1 kg∙m‐3 for T > 353 K, Uc(ρ) = 0.5 kg∙m‐3 for 313.15 K < T < 353 K, Uc(ρ) = 0.8 kg∙m‐3 for T < 313.15 K (0.95 level of confidence).