SUPPLEMENTARY MATERIAL TO

Synthesis, antioxidant, antimicrobial and antifungal activity of carbohydrazones

ALEKSANDRA R. BOŽIĆ,1 NENAD R. FILIPOVIĆ,2 IRENA T. NOVAKOVIĆ,3 SNEŽANA K. BJELOGRLIĆ,4 JASMINA B. NIKOLIĆ,5 SAŠA Ž. DRMANIĆ5 and ALEKSANDAR D. MARINKOVIĆ5

1Belgrade Polytechnic, Brankova 17, 11000 Belgrade, Serbia,,   2Faculty of Agriculture, University of Belgrade, Nemanjina 6, Belgrade, Serbia, 3Institute of Chemistry, Technology and Metallurgy, University of Belgrade, Njegoševa 12, Belgrade, Serbia, 4National Cancer Research Center of Serbia, Pasterova 14, Belgrade, Serbia, 5Faculty of Technology and Metallurgy, University of Belgrade, Karnegijeva 4, Belgrade, Serbia

SPECTRAL DATA FOR COMPOUNDS a1-a14

Salicylaldehyde carbohydrazones (a1)1. White solid (solvent used for crystallization: ethanol). Yield: 66 %; m.p. 180-181°C  (lit m.p. -);  Anal. Calcd. for C8H9N4O2 (Mw = 245.24 g mol–1): C, 49.74; H, 4.70; N, 29.00 %; Found: C, 49.68; H, 4.66; N, 28.93 %; IR (KBr, cm–1):  3353 (OH), 3282 (NH2), 3096 (NH), 1680 (C=O), 1640 (C=N).

Fig. S1. Equilibrium of tautomeric forms and geometrical isomers of a1 with numeration of the atom of

interest.

2-pyridylaldehyde carbohydrazones (a2). White solid (acetonitrile). Yield: 67 %; m.p. 173-174 oC. Anal. Calcd. for C7H9N5O (Mw = 179.18 g mol-1):  C, 46.92; H, 5.06; N, 39.09 %, Found: C, 46.88; H, 5.01; N, 39.11 %; IR (KBr, cm-1): 3313 (NH2), 3208 (NH), 1678 (C=O), 1635 (C=N); 1H NMR (500 MHz, DMSO-d6, δ / ppm)  4.11 (2H, s, H2–N5), 7.31 (1H,  ddd, H–C5, 3J5,4 = 7.5 Hz,  3J5,6 = 4.9 Hz), 7.78 (1H, td, H–C4, 3J4,3 = 7.9 Hz,  3J4,5 =7.5 Hz,  4J4,6 = 1.5 Hz), 7.89 (1H, s, H–C7), 8.284-8.105 (2H, br.m.ovlp., H–C3, H-N4,  3J3,4 = 7.9 Hz), 8.51 (1H, ddd, H–C6, 3J6,5 = 4.9 Hz, 4J6,4 = 1,5 Hz), 10.64 (1H, s, H–N3); 13C NMR (126 MHz, DMSO-d6, δ / ppm)  119.85 (C3), 123.69 (C5), 136.47 (C4), 140.59 (C7), 149.09 (C6), 153.77 (C2), 156.85 (C8); 15N NMR  (derived from 2D HMBC, δ / ppm):  51.1 (N5),  99.7 (N4), 153.6 (N3), 312.2 (N1), 326.0 (N2).

Fig. S2. (E)-isomer of compound a2 with numeration of atom of interest

Fig. S3. 2D 15N-HMBC spectrum of a2 in DMSO-d6 recorded at 298 K (abscissa 1H;  ordinate 15N NMR chemical shift)

Methyl 2-pyridyl ketone carbonohydrazone (a3)2. White solid (ethanol). Yield: 72,0 %; m.p. 203 oC. (lit m.p. 202-203°C);  Anal. Calcd. for C8H11N5O (Mw = 193.21 g mol-1): C, 47.73; H, 5.74; N, 36.25 %, Found: C, 47.61; H, 5.82; N, 36.18  %;  IR (KBr, cm-1): 3308 (NH2), 3197 (NH), 1674 (C=O), 1631 (C=N).

Phenyl 2-pyridyl ketone carbonohydrazone (a4). White solid (ethanol). Yield: 84 %; m.p. 203-205 oC; Anal. Calcd. for C13H13N5O (Mw = 255.11 g mol-1):  C, 61.17; H, 5.13; N, 27.43 %, Found: C, 61.02; H, 4.98; N, 27.15 %; IR (KBr, cm-1): 3304 (NH2), 3215 (NH), 1674 (C=O), 1623 (C=N); 1H NMR (500 MHz, DMSO-d6, δ / ppm)  4.15 (2H, s, H2–N5), 7.36 (1H,  dt, H–C5, 3J5,4 = 7.5 Hz,  3J5,6 = 4.8 Hz), 7.40-7.60 (5H, m, Ph), 7.68 (1H, td, H–C4, 3J4,3 = 7.8 Hz,  3J4,5 =7.2 Hz), 8.01 (1H, dd, H–C3, 3J3,4 = 7.8 Hz); 8.26 (1H, s, H-N4), 8.85 (1H, dd, H–C6, 3J6,5 = 4.8 Hz), 13.20 (1H, s, H–N3); 13C NMR (126 MHz, DMSO-d6, δ / ppm)  121.57 (C3), 123.88 (C5), 124.84 (Ph), 125.95 (Ph), 128.27 (Ph), 128.93(Ph), 129.14 (Ph), 138.18 (C4), 143.23 (C7), 148.90 (C6), 151.40 (C2), 157.21 (C8); 15N NMR  (derived from 2D HMBC, δ / ppm): 57.62 (N5), 100.07 (N4), 155.1 (N3), 306.33 (N1), 315.85 (N2).

Fig. S4. Equilibrium of tautomeric forms (a4-a, a4-c and a4-d) and geometrical isomers (a4-a and a4-b) of compound a4 with numeration of the atom of interest.

Fig. S5. 2D NOESY of a4 in DMSO-d6 recorded at 298 K (abscissa and ordinate 1H NMR chemical shift)

Fig. S6. 2D 15N-HMBC of a4 in DMSO-d6 at 298 K (abscissa 1H;  ordinate 15N NMR chemical shift)

2-Quinolinealdehyde carbohydrazone (a5)3. White solid (methanol). Yield: 56 %; m.p. 183 °C.   (lit m.p. 183°C);   Anal. Calcd. for C11H11N5O (Mw = 229.24 gmol–1): C, 57.63; H, 4.84; N, 30.55 %, Found: C, 57.58; H, 4.62; N, 30.69 %; IR (KBr, cm–1):  3297 (NH2), 3188 (NH), 1679 (C=O), 1638 (C=N).

8-Hydroxy-2-quinolinealdehyde carbohydrazone (a6)3. Yellow solid (methanol). Yield: 72 %; m.p. 214-215 °C.  (lit m.p. 214-215°C).   Anal. Calcd. for C11H11N5O2  (Mw = 245.24 g mol–1): C, 53.83; H, 4.525; N, 28.56 %, Found: C, 53.66; H, 4.68; N, 28.74 %; IR (KBr, cm–1):  3371 (OH), 3335 (NH2), 3198 (NH), 1696 (C=O), 1600 (C=N).

8-Quinolinealdehyde carbohydrazone (a7)3. Yellow solid (methanol). Yield: 64 %; m.p. 185 °C.   (lit m.p. 185°C);   Anal. Calcd. for C11H11N5O (Mw = 229.24 gmol–1): C, 57.63; H, 4.84; N, 30.55 %, Found: C, 57.71; H, 4.78; N, 30.62 %; IR (KBr, cm–1):  3316 (NH2), 3200 (NH), 1681 (C=O), 1621 (C=N).

bis(Salcylaldehyde) carbohydrazones (a8)4. Yelow cristal (ethanol). Yield: 78 %; m.p. 219°C  (lit m.p. 216°C);  Anal. Calcd. for C15H14N4O3  (Mw = 298.11 g mol–1): C, 60.35; H, 4.74; N, 18.79 %, Found: C, 60.22; H, 4.62; N, 18.93 %; IR (KBr, cm–1):  3344 (OH), 3284 (NH), 1704 (C=O), 1622 (C=N).

bis(2-pyridylaldehyd) carbohydrazones (a9)5. White solid (ethanol). Yield: 88 %; m.p. 185°C  (lit m.p. 190-191°C);  Anal. Calcd. for C13H12N6O (Mw = 268.11 g mol-1):  C, 58.20; H, 4.51; N, 31.33 %, Found: C, 58.12; H, 4.88; N, 30.98 %; IR (KBr, cm-1): 3201 (NH), 1696 (C=O), 1604 (C=N).

bis(Methyl 2-pyridyl ketone) carbonohydrazone (a10)2. White solid (ethanol). Yield: 88,0 %; m.p.(decomp.) 187 oC (lit M.p.(decomp.) 186°C);  Anal. Calcd. for C15H16N6O (Mw = 296.14 g mol-1): C, 60.80; H, 5.44; N, 28.36 %, Found: C, 60.61; H, 5.31; N, 28.62  %;  IR (KBr, cm-1): 3206 (NH), 1698 (C=O), 1611 (C=N).

bis(Phenyl 2-pyridyl ketone) carbonohydrazone (a11)2. White solid (ethanol). Yield: 91,0 %. M.p. 223 oC (lit M.p. 225-226°C).  Anal. Calcd. for C25H20N6O (Mw = 420.17 g mol-1): C, 71.41; H, 4.79; N, 19.99 %, Found: C, 71.16; H, 4.82; N, 20.04  %.  IR (KBr, cm-1): 3177 (NH), 1702 (C=O), 1612 (C=N).

bis(2-Quinolinealdehyde) carbohydrazone (a12)3. White solid (DMF/methanol mixture 1 : 9 v/v). Yield 78 %; m.p. 162-164 °C (lit m.p. 162-164°C); Anal. Calcd. for C21H16N6O (Mw = 368.14 g mol–1): C, 68.47; H, 4.38; N, 22.81 %, Found: C, 68.81; H, 4.80; N, 22.56 %; IR (KBr, cm–1): 3392 (NH), 1708 (C=O), 1630 (C=N).

bis(8-Hydroxy-2-quinolinealdehyde) carbohydrazone (a13)3. Yellow solid (DMF/methanol mixture 1 : 9 v/v). Yield: 66 %; m.p. 248-249 °C (lit m.p. 248-249°C); Anal. Calcd. for C21H16N6O3 (Mw = 400.39 gmol–1): C, 62.99; H, 4.03; N, 20.99, %, Found: C, 62.84; H, 4.11; N, 21.22 %; IR (KBr, cm–1): 3408 (OH), 3116 (NH), 1684 (C=O), 1601 (C=N).

bis(8-Quinolinealdehyde) carbohydrazone (a14)3. Yellow solid (methanol). Yield: 54 %; m.p. 219-220 °C (lit m.p. 219-220°C); Anal. Calcd. for C21H16N6O (Mw = 368.14 g mol–1): C, 68.47; H, 4.38; N, 22.81 %, Found: C, 68.32; H, 4.91; N, 22.73 %; IR (KBr, cm–1): 3331 (NH), 1707 (C=O), 1614 (C=N).

TABLE SI. In vitro antifungal activity of the compounds tested by the well-diffusion agar assay expressed as the diameter (mm) of the inhibition zone

| Tested compound | C. albicans | S. cerevisiae | A. brasiliensis |
| --- | --- | --- | --- |
| a1 | / | / | / |
| a2 | / | / | / |
| a3 | / | / | / |
| a4 | / | / | / |
| a5 | 10 | 14 | 12 |
| a6 | 12 | 14 | 12 |
| a7 | 12 | 16 | 16 |
| a8 | / | / | / |
| a9 | / | / | / |
| a10 | / | / | / |
| a11 | / | / | / |
| a12 | / | / | / |
| a13 | 12 | 10 | 10 |
| a14 | 14 | 10 | 10 |
| Nystatin | 34 | 56 | 32 |

REFERENCES

1. 	P. Novak, T. Jednačak, J. Parlov Vuković, K. Zangger, M. Rubčić, N. Galić, T. Hrenar, Croat. Chem. Acta 85 (2012) 451.

2. 	A. Bacchi, M. Carcelli, P. Pelagatti, C. Pelizzi, G. Pelizzi, 75 (1999) 123.

3. 	A. Božić, A. Marinković, S. Bjelogrlić, T. R. Todorović, I. N. Cvijetić, I. Novaković, C. D. Muller, N. R. Filipović, RSC Adv. 6 (2016) 104763.

4. 	D. Maity, A. K. Manna, D. Karthigeyan, T. K. Kundu, S. K. Pati, T. Govindaraju, Chem. - A Eur. J. 17 (2011) 11152.

5. 	A. Hoque, Md. Najbul Basu, G. Das, Cryst. Growth Des. 14 (2014) 6.